Copyright 2021 by The American Institute of Architects (AIA)

Exclusively published and distributed by Deltek, Inc. for the AIA

This Product MasterSpec Section is licensed by Deltek, Inc. to ClarkDietrich ("Licensee").

This Product MasterSpec Section modifies the original MasterSpec text and does not include the full content of the original MasterSpec Section.

Revisions made to the original MasterSpec text are made solely by the Licensee and are not endorsed by, or representative of the opinions of, Deltek or The American Institute of Architects (AIA). Neither AIA nor Deltek are liable in any way for such revisions or for the use of this Product MasterSpec Section by any end user. A qualified design professional should review and edit the document to suit project requirements.

For more information, contact ClarkDietrich, 9050 Centre Pointe Dr., Suite 400, West Chester, OH 45069; Phone: (513) 870-1100; Fax: (513) 870-1300; Website: www.clarkdietrich.com; Email: info@clarkdietrich.com.

For information about MasterSpec, contact Deltek at (800) 424-5080 or visit masterspec.com.

SECTION 092216 - NON-STRUCTURAL METAL FRAMING

TIPS:

To view non-printing Editor's Notes that provide guidance for editing, click on MasterWorks/Single-File Formatting/Toggle/Editor's Notes.

To read detailed research, technical information about products and materials, and coordination checklists, click on MasterWorks/Supporting Information.

Access Product MasterSpec Sections:

<Double click here to view the list of manufacturer Sections available at ProductMasterSpec.com>

Access product transparency content in the Sustainable Minds Transparency Catalog:

<Double click here to view products with environmental product declarations (EPDs) and material ingredient disclosures>

Access BIM Content on BIMsmith Market:

<Double click here to view products on BIMsmith Market>

Revise this Section by deleting and inserting text to meet Project-specific requirements.

MasterSpec includes provisions for LEED v4, LEED v4.1, IgCC, and Green Globes.

GENERAL

SUMMARY

Section Includes:

Non-load-bearing steel framing systems for interior partitions.

Suspension systems for interior ceilings and soffits.

Grid suspension systems for gypsum board ceilings.

Related Requirements:

Retain subparagraph below to cross-reference requirements Contractor might expect to find in this Section but are specified in another Section.

Section 054000 "Cold-Formed Metal Framing" for exterior and interior load-bearing, interior non-load-bearing wall framing exceeding height limitations, and exterior non-load-bearing wall studs; floor joists; and roof rafters and ceiling joists.

ACTION SUBMITTALS

Action submittals are submittals requiring responsive action and return of reviewed documents to Contractor.

Product Data: For each type of product.

Retain "Sustainable Design Submittals" Paragraph below if pursuing sustainable certification.

Sustainable Design Submittals:

Retain "Product Data" Subparagraph below to require minimum recycled content for LEED v4 or LEED v4.1, MRc "Building Project Disclosure and Optimization - Sourcing of Raw Materials, Option 2 - Leadership Extraction Practices, Recycled Content."

Product Data: For recycled content, indicating postconsumer and preconsumer recycled content and cost.

"Environmental Product Declaration (EPD)" Subparagraph below applies to LEED v4 (all), MRc "Building Product Disclosure and Optimization - Environmental Product Declarations." Verify, with manufacturer, that EPDs are available for each product.

Environmental Product Declaration (EPD): For each product.

"Construction and Demolition Waste Management" Subparagraph below applies to the following in LEED v4, MRc "Construction and Demolition Waste Management Planning":

Option 1, Path 1: Divert at least 50 percent of the total construction and demolition material; diverted materials must include at least three material streams.

Option 1, Path 2: Divert at least 75 percent of the total construction and demolition material; diverted materials must include at least four material streams.

Option 2: Reduction of total waste material.

Establish Project waste diversion goals by identifying five or more materials (both structural and nonstructural) targeted for diversion. Determine an approximate percentage of overall Project waste that these materials represent.

Specify whether materials will be separated or commingled and describe each diversion strategy planned for Project. Describe where materials will be taken and how recycling facility will process them.

Provide a final report detailing each major waste stream generated, including disposal and diversion rates.

Construction and Demolition Waste Management: For each product.

Retain "Health Product Declaration (HPD)" Paragraph below for LEED v4.1, MRc "Building Product Disclosure and Optimization - Material Ingredients."

Health Product Declaration (HPD): Provide documentation confirming product compliance with one of the following:

Option 1: Material Ingredient Reporting: Use at least 20 different permanently installed products from at least five different manufacturers that use one of the qualifying programs to demonstrate the chemical inventory of the product to at least 0.1 percent (1000 ppm).

Option 2: Material Ingredient Optimization: Use products that have a compliant material ingredient optimization report or action plan. Use at least five permanently installed products sourced from at least three different manufacturers.

INFORMATIONAL SUBMITTALS

Information submittals are submittals that require review by Architect, but they do not require Architect's responsive action and return of reviewed documents to Contractor, provided submittals comply with requirements. If rejected, submittals with responsive action must be returned to Contractor.

Retain "Product Certificates" Paragraph below to require submittal of product certificates from manufacturers.

Product Certificates: For each type of code-compliance certification for studs and tracks.

Evaluation Reports: Submit evaluation reports certified under an independent third-party inspection program administered by an agency accredited by IAS to ICC-ES AC98 accreditation criteria for inspection agencies.

Electronic submittals generated via ClarkDietrich's website and submitted electronically are acceptable, when electronic documentation is allowed per procedural requirements in Division 01. Electronic submittals can be generated at www.clarkdietrich.com.

Manufacturer's Certification: Submit manufacturer's certification of product compliance with codes and standards along with product literature and data sheets for specified products.

QUALITY ASSURANCE

Retain "Code-Compliance Certification of Studs and Tracks" Paragraph below for third-party verification that products comply with requirements of model codes and industry standards. Coordinate retained certification program(s) with the member companies in manufacturer lists. See "Code-Compliance Certification Programs" Article in the Evaluations.

Code-Compliance Certification of Studs and Tracks: Provide documentation that framing members are certified in accordance with the product-certification program of the Steel Framing Industry Association (SFIA) or similar organization providing a verifiable code-compliance program.

Contractor to provide effective, full-time quality control over fabrication and erection complying with pertinent codes and regulations of government agencies having jurisdiction. Conduct preinstallation meeting to verify Project requirements, substrate conditions, and manufacturer's written installation instructions.

DELIVERY, STORAGE, AND HANDLING

Notify manufacturer of damaged materials received prior to installation.

Deliver materials in manufacturer's original, unopened, undamaged containers with identification labels intact.

Protect cold-formed metal framing from corrosion, deformation, and other damage during delivery, storage, and handling as required by AISI S202.

PRODUCTS

Manufacturers and products listed in this Section are neither recommended nor endorsed by the AIA or Deltek. Before selecting manufacturers and products, verify availability, suitability for intended applications, and compliance with minimum performance requirements. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

Product options commonly available from manufacturers are included in square brackets throughout the Section Text. Not every manufacturer listed can provide every option offered; verify availability with manufacturers. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

PERFORMANCE REQUIREMENTS

Retain "Fire-Test-Response Characteristics" Paragraph below if framing is part of fire-resistance-rated assemblies. Indicate design designations of specific assemblies on Drawings.

Fire-Test-Response Characteristics: For fire-resistance-rated assemblies that incorporate non-load-bearing steel framing, provide materials and construction identical to those tested in assembly indicated, in accordance with ASTM E119 and displaying a classification label from an independent testing agency acceptable to authorities having jurisdiction.

Construct fire-resistance-rated partitions in compliance with tested assembly requirements[ indicated on Drawings].

Rated assemblies to be substantiated from applicable testing using proposed products, by Contractor.

Retain "STC-Rated Assemblies" Paragraph below if framing is part of STC-rated assemblies. Indicate design designations of specific assemblies on Drawings. The IBC requires ASTM E90 testing, and Gypsum Association's GA-600 uses ASTM E90 testing for its STC-rated assemblies.

STC-Rated Assemblies: For STC-rated assemblies, provide materials and construction identical to those tested in assembly indicated on Drawings, in accordance with ASTM E90 and classified in accordance with ASTM E413 by an independent testing agency.

Retain "Horizontal Deflection" Paragraph below to allow Contractor to choose stud base-steel thickness and stud spacing rather than specifying base-steel thickness and spacing or indicating them on Drawings. Coordinate deflection limit with partition finishes (for example, plaster, gypsum board, veneer plaster, etc.) and whether composite (full height, partition finishes to both sides) or non-composite (single-sided wall finish) assemblies.

Horizontal Deflection: For [composite] [non-composite] wall assemblies, limited to [1/240] [1/360] of the wall height based on horizontal loading of [5 lbf/sq. ft. (239 Pa)] [10 lbf/sq. ft. (480 Pa)] <Insert value>.

Retain first option in first paragraph below for IBC 2012; second option for IBC 2015; third option for IBC 2018 or IBC 2021.

Design framing systems in accordance with [ASTM C645] [AISI S220 and ASTM C645, Section 10] [AISI S220], unless otherwise indicated.

Design Loads: As indicated on architectural Drawings or 5 lbf/sq. ft. (239 Pa) minimum as required by the IBC.

Design framing systems to accommodate deflection of primary building structure and construction tolerances and to withstand design loads with a maximum deflection of <Insert inches (mm)>.

FRAMING SYSTEMS

Retain "Recycled Content of Steel Products" Paragraph below to specify recycled content if required. An alternative method of requiring recycled content is to retain requirement in Project's Division 01 sustainable design requirements Section that gives Contractor the option and responsibility to determine how recycled content requirements will be met.

Recycled Content of Steel Products: Postconsumer recycled content plus one-half of preconsumer recycled content not less than [25] <Insert number> percent.

Retain first option in "Framing Members, General" Paragraph below for IBC 2012; second option for IBC 2015; third option for IBC 2018 or IBC 2021.

Framing Members, General: Comply with [ASTM C645] [AISI S220 and ASTM C645, Section 10] [AISI S220] for conditions indicated.

Retain first option in "Steel Sheet Components" Subparagraph below for IBC 2012; second option for IBC 2015; third option for IBC 2018 or IBC 2021.

Steel Sheet Components: Comply with [ASTM C645] [AISI S220 and ASTM C645, Section 10] [AISI S220] requirements for metal unless otherwise indicated

See "Corrosion Protection of Steel Framing" and "Code-Compliance Certification Programs" articles in the Evaluations for a discussion of corrosion-resistant coatings on components and their certification.

Retain first option in "Protective Coating" Subparagraph below for IBC 2012; retain second option for IBC 2015, IBC 2018, or IBC 2021.

Protective Coating: Comply with [ASTM C645] [AISI S220]; ASTM A653/A653M, G40 (Z120); or coating with equivalent corrosion resistance. Galvannealed products are unacceptable.

Coating to demonstrate equivalent corrosion resistance with an evaluation report acceptable to authorities having jurisdiction.

Retain "Basis-of-Design Product" Subparagraph below to identify a specific product.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; DiamondPlus Coating on ProSTUD and ProTRAK [25] [20].

Retain first option in "Studs and Track" Paragraph below for IBC 2012; second option for IBC 2015; third option for IBC 2018 or IBC 2021.

Studs and Track: [ASTM C645] [AISI S220 and ASTM C645, Section 10] [AISI S220].

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; ProSTUD Drywall Framing System with Smart Edge technology or comparable product by one of the following current members of the SFIA:

CEMCO; California Expanded Metal Products Co.

Telling Industries.

<Insert manufacturer's name>.

Retain first option in "Minimum Base-Steel Thickness" Subparagraph below for ClarkDietrich's "ProSTUD/ProTRAK 25" at 50 ksi.

Retain second option for "ProSTUD/ProTRAK 20" (ProSTUD 20 at 70 ksi and ProTRAK 20 at 50 ksi).

Retain third option for "ProSTUD/ProTRAK 30" at 33 ksi.

Retain fourth option for "ProSTUD/ProTRAK 33" at 33 ksi.

Minimum Base-Steel Thickness: [0.0150 inch (0.3810 mm)] [0.0181 inch (0.4597 mm)] [0.0296 inch (0.7518 mm)] [0.0329 inch (0.8382 mm)].

Flange Size: 1-1/4 inches (32 mm).

Web Depth: [As indicated on Drawings] [3-5/8 inches (92 mm)] [6 inches (152 mm)] [4 inches (102 mm)] [2-1/2 inches (64 mm)] [1-5/8 inches (41 mm)].

Steel Framing Stud and Track Wall System: Self-locking steel studs, and telescoping stud extensions and tracks.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; TRAKLOC [Adjustable Stud (TLA)] [Elevator Stud (TLE)] [Fixed Length Stud (TLF)] [Track (TTS)] Steel Framing System or comparable product by a current member of the SFIA:

<Insert manufacturer's name>.

Minimum Base-Steel Thickness: [0.0238 inch (0.60 mm)] [0.0296 inch (0.75 mm)] [0.0329 inch (0.84 mm)].

Depth: [2-1/2 inches (64 mm)] [3-5/8 inches (92 mm)] [4 inches (102 mm)] [6 inches (152 mm)].

Steel Framing Stud and Deflection Track Wall System: Self-locking steel studs with telescoping stud extension with knockout in each flange to allow for 1 inch (25 mm) of deflection for fire-rated head-of-wall deflection system.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; TRAKLOC Deflection Stud (TLD) and TRAKLOC Track (TTS) or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Minimum Base-Steel Thickness: [0.0238 inch (0.60 mm)] [0.0296 inch (0.75 mm)] [0.0329 inch (0.84 mm)].

Web Depth: [2-1/2 inches (64 mm)] [3-5/8 inches (92 mm)] [4 inches (102 mm)] [6 inches (152 mm)].

For slip joint at stud and top-track interface (head joint) that avoids axial loading of partition by overhead structure, retain "Slip-Type Head Joints" Paragraph below and one or all of the following types of head joints. See "Crack Control" Article in the Evaluations.

Slip-Type Head Joints: Where indicated, provide[ one of] the following:

If retaining "Clip System" Subparagraph below, indicate depth of tracks on Drawings or insert requirements. Clips can be used with tracks with standard legs and long legs.

Clip System: Clips designed for use in head-of-wall deflection conditions that provide a positive attachment of studs to tracks while allowing [1-1/2-inch (38-mm)] [2-inch (51-mm)] [2-1/2-inch (64-mm)] <Insert dimension> minimum vertical movement.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; Fast Top Clip [FTC3] [FTC5] or comparable product by one of the following current members of the SFIA:

CEMCO; California Expanded Metal Products Co.

Steel Network, Inc. (The).

<Insert manufacturer's name>.

Single Long-Leg Track System: Top track with 2-inch- (51-mm-) deep flanges in thickness not less than indicated for studs, installed with studs friction fit into top track and with continuous bridging and spacer bar located within 12 inches (305 mm) of the top of studs to provide lateral bracing.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; Deep Leg Deflection Track and Spazzer 9200 Bridging and Spacer Bar or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Slotted Deflection Track: Steel sheet top track manufactured to prevent cracking of finishes applied to interior partition framing resulting from deflection of structure above; in thickness not less than indicated for studs and in width to accommodate depth of studs.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; MaxTrak Slotted Deflection Track or comparable product by one of the following current members of the SFIA:

CEMCO; California Expanded Metal Products Co.

Telling Industries.

<Insert manufacturer's name>.

"Firestop Tracks" Paragraph below specifies firestop-type tracks for isolating partition framing from structure above in specific fire-resistance-rated assemblies. Products listed may need additional materials to achieve a fire-resistance rating; verify with manufacturer. If retaining, revise to coordinate with rated assemblies and indicate design designations of assemblies on Drawings.

Firestop Tracks: Top track manufactured to allow partition heads to expand and contract with movement of structure while maintaining continuity of fire-resistance-rated assembly indicated; in thickness not less than indicated for studs and in width to accommodate depth of studs.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; BlazeFrame [BlazeFrame DL] [BlazeFrame DSL] [BlazeFrame RipTRAK] [UltraBEAD with UltraTRAK Slotted System] [UltraBEAD with Deep Leg Deflection Track] or comparable product by one of the following current members of the SFIA:

CEMCO; California Expanded Metal Products Co.

Steel Network, Inc. (The).

<Insert manufacturer's name>.

Retain "Backing Plate" Paragraph below for proprietary fire-retardant-treated blocking and bracing for fixture attachment.

Backing Plate: Proprietary fire-retardant-treated wood blocking and bracing in width indicated.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; Danback Fire-Retardant Treated Wood Backing Plate [D16F] [D24F] or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Retain "Flat Strap and Backing Plate" Paragraph below for flat-strap blocking and bracing for fixture attachment. Indicate locations, lengths, and widths on Drawings.

Flat Strap and Backing Plate: Steel sheet for blocking and bracing in length and width indicated.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; Backing Plate or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Minimum Base-Steel Thickness: [As indicated on Drawings] [0.0179 inch (0.45 mm)] [0.0296 inch (0.752 mm)].

Retain "Channel Bridging and Bracing" or "U-Channel Bridging" Paragraph below for channel bridging for fixture attachment or lateral bracing. Indicate locations and details of installation on Drawings.

Channel Bridging and Bracing: Pre-notched steel, 7/8 by 7/8 by 50 inches (22.2 by 22.2 by 1270 mm), 0.0329-inch- (0.84-mm-) minimum base-steel thickness.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; Spazzer 9200 Bridging and Spacing Bar or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

U-Channel Bridging: Steel, 0.0538-inch- (1.37-mm-) minimum base-steel thickness, with minimum 1/2-inch- (13-mm-) wide flanges.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; Cold-Formed U-Channel and [Channel Clip (CC33)] [FastBridge (FB33)] Bridging Clip or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Retain first option in "U-Channel Depth" Subparagraph below for ClarkDietrich's "Channel Clip (CC33)"; second option for "FastBridge (FB33)."

U-Channel Depth: [3/4 inch (19 mm)] [1-1/2 inches (38 mm)] [As indicated on Drawings].

Rigid Furring Channels: Hat-shaped channels for furring out walls.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; Furring Channel or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Minimum Base-Steel Thickness: [As indicated on Drawings] [0.0179 inch (0.45 mm)] [0.0296 inch (0.75 mm)] <Insert thickness>.

Depth: [As indicated on Drawings] [7/8 inch (22.2 mm)] [1-1/2 inches (38 mm)].

Resilient Furring Channels: 1/2-inch- (13-mm-) deep, steel sheet members designed to reduce sound transmission.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; RC Deluxe (RCSD) Resilient Channel or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Configuration: Asymmetrical.

Sound Isolation Clips: Use with 18-mil (0.457-mm), 25-gauge, drywall furring channels for acoustical separation.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; Sound Clip (CDSC) or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Carrying Channels: 0.053-inch (1.34-mm) base-steel thickness, with minimum 1/2-inch- (13-mm-) wide flanges.

Depth: [As indicated on Drawings] [3/4 inch (19 mm)] <Insert depth>.

Furring Brackets: Adjustable, corrugated-edge-type steel sheet with minimum base-steel thickness of 0.0296 inch (0.75 mm).

Tie Wire: ASTM A641/A641M, Class 1 zinc coating, soft temper, 0.062-inch- (1.57-mm-) diameter wire, or double strand of 0.048-inch- (1.21-mm-) diameter wire.

Z-shaped furring is available in 1-, 1-1/2-, 2-, 2-1/2-, and 3-inch (25-, 38-, 51-, 64-, and 76-mm) depths. Coordinate Z-shaped furring requirements with insulation specified in Section 072100 "Thermal Insulation."

Z-Shaped Furring: With slotted or nonslotted web, face flange of 1-1/4 inches (32 mm), wall attachment flange of 3/4 inch (19 mm), minimum base-steel thickness of 0.0179 inch (0.455 mm), and depth required to fit insulation thickness indicated.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; Z-Furring Channel or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Radius Framing: Steel sheet runner for non-load-bearing curves, bends, variable radii, and arches.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; 360TRAK or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Minimum Base-Steel Thickness: [As indicated on Drawings] [0.0296 inch (0.75 mm)].

Depth: [As indicated on Drawings] [2-1/2 inches (63.5 mm)] [3-5/8 inches (92.1 mm)] [4 inches (101.6 mm)] [6 inches (152.4 mm)] <Insert depth>.

Headers and Jambs: Manufacturer's proprietary shape used to form header beams and jambs, columns or posts, of web depths indicated, unpunched, with stiffened flanges and as follows:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; Heavy-Duty Studs (HDS) and Type HDSC Header Bracket or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Minimum Base-Steel Thickness: [As indicated on Drawings] [0.0329 inch (0.84 mm)] [0.0428 inch (1.09 mm)] [0.0538 inch (1.37 mm)] [0.0677 inch (1.72 mm)] [0.0966 inch (2.45 mm)].

Retain "Web Size" or "Flange Size" Subparagraph below, or both, to suit Project.

Web Size: [3-5/8 inches (92.1 mm)] [4 inches (102 mm)] [6 inches (152 mm)] [8 inches (203 mm)].

Flange Size: 3 inches (76.2 mm).

Framed Openings: Galvanized-steel, one-piece header and jamb studs in lieu of built-up members.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; RedHeader PRO and Type HDSC Header Bracket or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Minimum Base-Steel Thickness: [0.0329 inch (0.84 mm)] [0.0428 inch (1.09 mm)] [0.0538 inch (1.37 mm)] [0.0677 inch (1.72 mm)] [0.0966 inch (2.45 mm)] [As required by design].

Web Size: [3-5/8 inches (92 mm)] [4 inches (102 mm)] [6 inches (152 mm)] [8 inches (203 mm)].

Flange Width: [3 inches (76.2 mm)] [3-1/2 inches (88.9 mm)].

Type HDSC Header Bracket: Size as required by design.

Minimum Base-Steel Thickness: [0.0329 inch (0.84 mm)] [0.0677 inch (1.72 mm)] [0.0966 inch (2.45 mm)].

Shaftwall System: Non-load-bearing fire-rated wall assemblies that provide critical, life-safety, fire-resistant protection for elevator shafts, stairwells, vertical chases, and mechanical enclosures.

Stud: Manufacturer's standard profile for repetitive members, corner and end members, and fire-resistance-rated assembly indicated below:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; CT Stud or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Depth: [2-1/2 inches (63.5 mm)] [4 inches (102 mm)] [6 inches (152.4 mm)] [As indicated].

Minimum Base-Steel Thickness: [0.0219 inch (0.56 mm)] [0.0329 inch (0.84 mm)] [As indicated].

Runner Tracks: Manufacturer's standard J-profile track with 2-1/4-inch (57.1-mm) leg and matching studs in depth.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; J-Tabbed Track or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Minimum Base-Steel Thickness: [0.0219 inch (0.56 mm)] [0.0329 inch (0.84 mm)] [As indicated].

Retain first option in "Partial Wall Framing Connection" Paragraph below for ClarkDietrich's "LGPW" series.

Retain second option for "PW" series.

Partial Wall Framing Connection: [3/8-inch (9.5-mm)] [1/2-inch (12.7-mm)] ASTM A36/A36M steel-plate ST50H stud connector designed to support out-of-plane loading of cantilevered partial wall systems that are unsupported at the top track.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; Pony Wall [LGPW24] [LGPW36] [LGPW48] [LGPW60] [PW24] [PW36] [PW48] or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Retain first option in "Minimum Base-Steel Thickness" Subparagraph below for ClarkDietrich's "LGPW" series.

Retain second option for "PW" series.

Minimum Base-Steel Thickness: [0.0538 inch (1.37 mm)] [0.0966 inch (2.45 mm)].

Retain first "Size (Height; Width by Length)" Subparagraph below for ClarkDietrich's "LGPW" series.

Size (Height; Width by Length): [23-5/8 inches (600 mm)] [35-5/8 inches (905 mm)] [47-5/8 inches (1210 mm)] [59-5/8 inches (1514 mm)] tall; with 2-3/8-by-5-1/2-inch (60-by-140-mm) long plate.

Retain "Size (Height; Width by Length)" Subparagraph below for ClarkDietrich's "PW" series.

Size (Height; Width by Length): [23-3/4 inches (603 mm)] [35-3/4 inches (908 mm)] [47-3/4 inches (1213 mm)] tall; with 3-3/8-by-8-inch (86-by-203-mm) long plate.

SUSPENSION SYSTEMS

Retain this article for suspended or furred ceilings or soffits and for grid suspended ceilings.

Tie Wire: ASTM A641/A641M, Class 1 zinc coating, soft temper, 0.062-inch- (1.59-mm-) diameter wire, or double strand of 0.048-inch- (1.21-mm-) diameter wire.

Hanger Attachments to Concrete:

ICC-ES AC01 and AC193 are for expansion anchors in masonry and mechanical anchors in concrete, respectively, and AC58 and AC308 are for adhesive anchors in masonry and concrete. Do not use expansion-type anchors where expansion can cause damage to the substrate material. Verify with Project's structural engineer, and insert specific load requirements and names of acceptable products if required.

Post-Installed Anchors: Fastener systems with an evaluation report acceptable to authorities having jurisdiction, based on ICC-ES [AC01] [AC193] [AC58] [or] [AC308] as appropriate for the substrate.

Uses: Securing hangers to structure.

Retain "Type" Subparagraph below to restrict type of anchor if required.

Type: [Torque-controlled, expansion anchor] [torque-controlled, adhesive anchor] [or] [adhesive anchor].

Material in "Material for Interior Locations" Subparagraph below protects against corrosion in an indoor atmosphere.

Material for Interior Locations: Carbon-steel components zinc-plated to comply with ASTM B633 or ASTM F1941 (ASTM F1941M), Class Fe/Zn 5, unless otherwise indicated.

Alloy Group 1 (A1) refers to Type 304 and similar alloys, and Alloy Group 2 (A4) refers to Type 316 and similar alloys.

Material for Exterior or Interior Locations and Where Stainless Steel Is Indicated: Alloy [Group 1 (A1)] [Group 2 (A4)] stainless steel bolts, ASTM F593, and nuts, ASTM F594.

Retain "Power-Actuated Anchors" Subparagraph below if power-actuated fasteners are acceptable. Verify with Project's structural engineer, and insert specific load requirements and names of acceptable products if required.

Power-Actuated Anchors: Fastener systems with an evaluation report acceptable to authorities having jurisdiction, based on ICC-ES AC70.

Retain "Wire Hangers" or "Flat Hangers" Paragraph below, or insert requirements to suit Project. Verify requirements of authorities having jurisdiction. If more than one type of hanger is required, indicate locations of each on Drawings.

Wire Hangers: ASTM A641/A641M, Class 1 zinc coating, soft temper, 0.16 inch (4.06 mm) in diameter.

Flat Hangers: Steel sheet, [in size indicated on Drawings] [1 by 3/16 inch (25 by 5 mm) by length indicated] <Insert size>.

Retain "Carrying Channels (Main Runners)" Paragraph below for conventional ceiling suspension framing; delete if only grid suspension ceilings are required.

Carrying Channels (Main Runners): Cold-formed, commercial-steel sheet with a base-steel thickness of 0.0538 inch (1.367 mm) and minimum 1/2-inch- (13-mm-) wide flanges.

Depth: [As indicated on Drawings] [2 inches (51 mm)] [1-1/2 inches (38 mm)] [3/4 inch (19 mm)].

Furring Channels (Furring Members):

Retain one type of furring member below or, if more than one is required, indicate locations of each on Drawings.

Cold-Formed Channels: 0.0538-inch (1.367-mm) base-steel thickness, with minimum 1/2-inch- (13-mm-) wide flanges, 3/4 inch (19 mm) deep.

Retain first option in "Steel Studs and Tracks" Subparagraph below for IBC 2012; second option for IBC 2015; third option for IBC 2018 or IBC 2021.

Steel Studs and Tracks: [ASTM C645] [AISI S220 and ASTM C645, Section 10] [AISI S220].

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; ProSTUD Drywall Framing System with Smart Edge technology or comparable product by one of the following current members of the SFIA:

CEMCO; California Expanded Metal Products Co.

Telling Industries.

<Insert manufacturer's name>.

Retain first option in "Minimum Base-Steel Thickness" Subparagraph below for ClarkDietrich's "ProSTUD/ProTRAK 25" at 50 ksi.

Retain second option for "ProSTUD/ProTRAK 20" (ProSTUD 20 at 70 ksi and ProTRAK 20 at 50 ksi).

Retain third option for "ProSTUD/ProTRAK 30" at 33 ksi.

Retain fourth option for "ProSTUD/ProTRAK 33" at 33 ksi.

Minimum Base-Steel Thickness: [0.0150 inch (0.3810 mm)] [0.0181 inch (0.4597 mm)] [0.0296 inch (0.752 mm)] [0.0329 inch (0.836 mm)].

Flange Size: 1-1/4 inches (32 mm).

Web Depth: [As indicated on Drawings] [1-5/8 inches (41 mm)] [2-1/2 inches (64 mm)] [3-5/8 inches (92 mm)].

Retain first option in "Hat-Shaped, Rigid Furring Channels" Subparagraph below for IBC 2012; second option for IBC 2015, IBC 2018, or IBC 2021.

Hat-Shaped, Rigid Furring Channels: [ASTM C645] [AISI S220], 7/8 inch (22 mm) deep.

Minimum Base-Steel Thickness: [As indicated on Drawings] [0.0179 inch (0.45 mm)] [0.0296 inch (0.752 mm)] <Insert thickness>.

Resilient Furring Channels: 1/2-inch- (13-mm-) deep members designed to reduce sound transmission.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide ClarkDietrich; RC Deluxe (RCSD) Resilient Channel or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Configuration: Asymmetrical.

Grid suspension systems are suitable for use with gypsum board. They might be unacceptable for gypsum veneer plaster; consult gypsum veneer plaster and grid suspension system manufacturers.

Grid Suspension System for Gypsum Board Ceilings: ASTM C645, direct-hung system composed of main beams and cross-furring members that interlock.

Retain "Products" Subparagraph and list of manufacturers and products below to require specific products or a comparable product from other manufacturers.

Manufacturers: Subject to compliance with requirements, provide products by one of the following:

Armstrong World Industries, Inc.

Chicago Metallic Corporation.

United States Gypsum Company.

<Insert manufacturer's name>.

AUXILIARY MATERIALS

General: Provide auxiliary materials that comply with referenced installation standards.

Fasteners for Steel Framing: Of type, material, size, corrosion resistance, holding power, and other properties required to fasten steel members to substrates.

Isolation Strip at Exterior Walls: Provide[ one of] the following:

Retain "Asphalt-Saturated Organic Felt" and "Foam Gasket" subparagraphs below and option in "Isolation Strip at Exterior Walls" Paragraph above to allow Contractor to choose type of isolation strip.

Asphalt-Saturated Organic Felt: ASTM D226/D226M, Type I (No. 15 asphalt felt), nonperforated.

Foam Gasket: Adhesive-backed, closed-cell vinyl foam strips that allow fastener penetration without foam displacement, 1/8 inch (3.2 mm) thick, in width to suit steel stud size.

Drywall Penetration Barrier Mesh: Supply and install barrier mesh, steel, expanded-metal panels as a penetration barrier behind gypsum wallboard walls and/or ceilings, where indicated on Drawings.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide Barrier Mesh supplied by ClarkDietrich; [BM50-13F Maximum Security] [BM75-9F Maximum Security] [BM15-9F Medium Security] [BM75-13F Medium Security] [BM10-16F Minimum Security] or comparable product by one of the following current members of the SFIA:

<Insert manufacturer's name>.

Finished shape of mesh openings is a flattened diamond, per ASTM F1267, Style 2.

"Barrier mesh" in "Barrier-Mesh Clips" Subparagraph below refers to ClarkDietrich's "BM-Type" clips.

Barrier-Mesh Clips: Barrier mesh is attached to framing members using barrier-mesh clips and appropriate threaded fasteners.

For steel framing, install a flat-head, bugle-type, self-tapping, fine-thread screw long enough to penetrate the framing member a minimum of 3/8 inch (9.5 mm).

For wood framing applications, install 1-5/8-inch (42-mm) fine-thread drywall screw allowing the fastener to penetrate the framing member at least 1-1/2 inches (38 mm).

"Clips" in subparagraph below refer to ClarkDietrich's "BM-Type" clips.

In ceiling applications, space clips a minimum of [6 inches (152 mm)] [12 inches (305 mm)] along ceiling joists.

Insert additional auxiliary materials, such as partition and outlet box isolation pads to maintain acoustic isolation, here.

EXECUTION

EXAMINATION

Examine areas and substrates, with Installer present, and including welded hollow-metal frames, cast-in anchors, and structural framing, for compliance with requirements and other conditions affecting performance of the Work.

Proceed with installation only after unsatisfactory conditions have been corrected.

PREPARATION

Delete "Suspended Assemblies" Paragraph below if only postinstalled anchors are used for installing suspended assemblies.

Suspended Assemblies: Coordinate installation of suspension systems with installation of overhead structure to ensure that inserts and other provisions for anchorages to building structure have been installed to receive hangers at spacing required to support the Work and that hangers will develop their full strength.

Furnish concrete inserts and other devices indicated to other trades for installation in advance of time needed for coordination and construction.

Coordination with Sprayed Fire-Resistive Materials:

Indicate requirements on Drawings for attaching steel framing to construction protected by sprayed fire-resistive materials.

Before sprayed fire-resistive materials are applied, attach offset anchor plates or ceiling tracks to surfaces indicated to receive sprayed fire-resistive materials. Where offset anchor plates are required, provide continuous plates fastened to building structure not more than 24 inches (610 mm) o.c.

After sprayed fire-resistive materials are applied, remove them only to extent necessary for installation of non-load-bearing steel framing. Do not reduce thickness of fire-resistive materials below that are required for fire-resistance ratings indicated. Protect adjacent fire-resistive materials from damage.

INSTALLATION, GENERAL

Installation Standard: ASTM C754.

Standards listed in "Gypsum Plaster Assemblies," "Portland Cement Plaster Assemblies," "Gypsum Veneer Plaster Assemblies," and "Gypsum Board Assemblies" subparagraphs below include framing installation requirements not in ASTM C754. Retain applicable subparagraphs to suit Project.

Gypsum Plaster Assemblies: Also comply with requirements in ASTM C841 that apply to framing installation.

Portland Cement Plaster Assemblies: Also comply with requirements in ASTM C1063 that apply to framing installation.

Gypsum Veneer Plaster Assemblies: Also comply with requirements in ASTM C844 that apply to framing installation.

Gypsum Board Assemblies: Also comply with requirements in ASTM C840 that apply to framing installation.

Install framing and accessories plumb, square, and true to line, with connections securely fastened.

Install supplementary framing, and blocking to support fixtures, equipment services, heavy trim, grab bars, toilet accessories, furnishings, or similar construction.

Install bracing at terminations in assemblies.

Indicate control and expansion joints on Drawings.

Do not bridge building control and expansion joints with non-load-bearing steel framing members. Frame both sides of joints independently.

INSTALLATION OF FRAMED ASSEMBLIES

Install framing system components in accordance with spacings indicated, but not greater than spacings required by referenced installation standards for assembly types.

Generally, indicate stud spacings on Drawings and delete "Single-Layer Application," "Multilayer Application," and "Tile Backing Panels" subparagraphs below. Retain first option in each of these subparagraphs if retaining "Horizontal Deflection" Paragraph in "Performance Requirements" Article. ASTM C754 includes tabulations of maximum framing spacing based on thickness and orientation of gypsum board panels and deflection and lateral loading.

Single-Layer Application: [As required by horizontal deflection performance requirements] [16 inches (406 mm) o.c.] [24 inches (610 mm) o.c.] unless otherwise indicated.

Multilayer Application: [As required by horizontal deflection performance requirements] [16 inches (406 mm) o.c.] [24 inches (610 mm) o.c.] unless otherwise indicated.

Tile Backing Panels: [As required by horizontal deflection performance requirements] [16 inches (406 mm) o.c.] unless otherwise indicated.

Retain first paragraph below if studs abut dissimilar metals at exterior walls or exterior masonry walls that may become damp.

Where studs are installed directly against exterior masonry walls or dissimilar metals at exterior walls, install isolation strip between studs and exterior wall.

Install studs so flanges within framing system point in same direction.

Install tracks at floors and overhead supports. Extend framing full height to structural supports or substrates above suspended ceilings except where partitions are indicated to terminate at suspended ceilings. Continue framing around ducts that penetrate partitions above ceiling.

Indicate locations and details of slip-type and fire-rated head joints on Drawings. See "Crack Control" Article in the Evaluations.

Slip-Type Head Joints: Where framing extends to overhead structural supports, install to produce joints at tops of framing systems that prevent axial loading of finished assemblies.

Door Openings: Screw vertical studs at jambs to jamb anchor clips on door frames; install track section (for cripple studs) at head and secure to jamb studs.

Usually, retain first subparagraph below. Design framing for doors more than 48 inches (1219 mm) wide, for double doors, and for extra-heavy doors to meet loading conditions.

Install two studs at each jamb unless otherwise indicated.

Retain first subparagraph below if one-piece control joints are required at heads of doors.

Install cripple studs at head adjacent to each jamb stud, with a minimum 1/2-inch (13-mm) clearance from jamb stud to allow for installation of control joint in finished assembly.

Retain first subparagraph below if suspended ceilings cannot withstand forces generated by opening and closing doors.

Extend jamb studs through suspended ceilings and attach to underside of overhead structure.

Retain "Other Framed Openings" Subparagraph below for framed openings other than doors, or revise to suit Project. Fully indicate framing for large openings on Drawings.

Other Framed Openings: Frame openings other than door openings the same as required for door openings unless otherwise indicated. Install framing below sills of openings to match framing required above door heads.

Fire-Resistance-Rated Partitions: Install framing to comply with fire-resistance-rated assembly indicated and support closures and to make partitions continuous from floor to underside of solid structure.

            - Install fire-resistant partitions using manufacturer's proprietary equivalent-gauge studs in compliance with requirements of [UL U419] [UL V450] [UL V438].

Indicate locations and details of firestop track on Drawings.

Firestop Track: Where indicated, install to maintain continuity of fire-resistance-rated assembly indicated.

Sound-Rated Partitions: Install framing to comply with sound-rated assembly indicated.

Curved Partitions:

Bend track to uniform curve and locate straight lengths so they are tangent to arcs.

Begin and end each arc with a stud, and space intermediate studs equally along arcs. On straight lengths of no fewer than two studs at ends of arcs, place studs 6 inches (152.4 mm) o.c.

Direct Furring:

Screw to wood framing.

Attach to concrete or masonry with stub nails, screws designed for masonry attachment, or powder-driven fasteners spaced 24 inches (610 mm) o.c.

Z-Shaped Furring Members:

Erect insulation, specified in Section 072100 "Thermal Insulation," vertically and hold in place with Z-shaped furring members spaced [24 inches (610 mm)] <Insert dimension> o.c.

Except at exterior corners, securely attach narrow flanges of furring members to wall with concrete stub nails, screws designed for masonry attachment, or powder-driven fasteners spaced 24 inches (610 mm) o.c.

At exterior corners, attach wide flange of furring members to wall with short flange extending beyond corner; on adjacent wall surface, screw-attach short flange of furring channel to web of attached channel. At interior corners, space second member no more than 12 inches (305 mm) from corner and cut insulation to fit.

"Installation Tolerance" Paragraph below is based on recommendation in GA-216 for wood framing and in ASTM C840 for steel framing.

Installation Tolerance: Install each framing member so fastening surfaces vary not more than 1/8 inch (3 mm) from the plane formed by faces of adjacent framing.

INSTALLATION OF CEILING SUSPENSION SYSTEMS

Install suspension system components in accordance with spacings indicated, but not greater than spacings required by referenced installation standards for assembly types.

Generally, indicate suspension system component spacing on Drawings and delete "Hangers," "Carrying Channels (Main Runners)," and "Furring Channels (Furring Members)" subparagraphs below. ASTM C754 includes tabulations of suspension system component size and spacing based on supported ceiling area at a uniform load of 4 lbf/sq. ft. (0.19 kPa).

Hangers: [48 inches (1219 mm)] <Insert dimension> o.c.

Retain "Carrying Channels (Main Runners)" Subparagraph below for conventional ceiling suspension framing; delete if only grid suspension ceilings are required.

Carrying Channels (Main Runners): [48 inches (1219 mm)] <Insert dimension> o.c.

Furring Channels (Furring Members): [16 inches (406 mm)] [24 inches (610 mm)] <Insert dimension> o.c.

Isolate suspension systems from building structure where they abut or are penetrated by building structure to prevent transfer of loading imposed by structural movement.

Suspend hangers from building structure as follows:

Install hangers plumb and free from contact with insulation or other objects within ceiling plenum that are not part of supporting structural or suspension system.

Splay hangers only where required to miss obstructions and offset resulting horizontal forces by bracing, countersplaying, or other equally effective means.

Where width of ducts and other construction within ceiling plenum produces hanger spacings that interfere with locations of hangers required to support standard suspension system members, install supplemental suspension members and hangers in the form of trapezes or equivalent devices.

Size supplemental suspension members and hangers to support ceiling loads within [performance limits established by referenced installation standards] <Insert deflection limit>.

Wire Hangers: Secure by looping and wire tying, either directly to structures or to inserts, eye screws, or other devices and fasteners that are secure and appropriate for substrate, and in a manner that will not cause hangers to deteriorate or otherwise fail.

Flat Hangers: Secure to structure, including intermediate framing members, by attaching to inserts, eye screws, or other devices and fasteners that are secure and appropriate for structure and hanger, and in a manner that will not cause hangers to deteriorate or otherwise fail.

Retain applicable construction types below.

Do not attach hangers to steel roof deck.

Do not attach hangers to permanent metal forms. Furnish cast-in-place hanger inserts that extend through forms.

Do not attach hangers to rolled-in hanger tabs of composite steel floor deck.

Do not connect or suspend steel framing from ducts, pipes, or conduit.

Furring channels must be wire tied to supports in most fire-resistance-rated assemblies. Verify requirements of fire-resistance-rated assemblies and revise "Fire-Resistance-Rated Assemblies" Paragraph below to suit Project.

Fire-Resistance-Rated Assemblies: Wire tie furring channels to supports.

Retain "Seismic Bracing" Paragraph below for seismic bracing and revise to include specific provisions to suit Project.

Seismic Bracing: Sway-brace suspension systems [with hangers used for support] <Insert requirements>.

Grid suspension systems are suitable for use with gypsum board. They might be acceptable for gypsum veneer plaster; consult gypsum veneer plaster and grid suspension system manufacturers.

Grid Suspension Systems: Attach perimeter wall track or angle where grid suspension systems meet vertical surfaces. Mechanically join main beam and cross-furring members to each other and butt-cut to fit into wall track.

Example tolerance in "Installation Tolerances" Paragraph below is based on ASTM C636 for acoustical ceilings.

Installation Tolerances: Install suspension systems that are level to within [1/8 inch in 12 ft. (3 mm in 3.6 m)] <Insert dimensions> measured lengthwise on each member that will receive finishes and transversely between parallel members that will receive finishes.

INSTALLATION OF DRYWALL PENETRATION BARRIER MESH

Install drywall penetration barrier mesh as follows:

Install barrier-mesh sheets with diamond running in direction most suitable.

Install barrier-mesh clips to secure mesh to framing members.

[Join staggered] [Butt] mesh joints that occur on framing members.

Overlapping mesh joints to achieve tie-in is acceptable.

Install barrier-mesh sheets to join, begin, and terminate on framing members.

Wire tie barrier-mesh sheets not joining on framing member with 0.046-inches (1.16-mm), 18-gauge, steel tie wire.

Wire tying to be no less frequent than mesh clip installation.

END OF SECTION 092216